## Slide 1: Interlude - GPUs
Fraser Macfarlane, Iain Milne

## Slide 2: What is a GPU?
Graphics Processing Unit
  Graphics/Gaming
  Video Editing + Rendering
Scientific Computing
  Bioinformatics
  Image Processing
  Machine Learning

## Slide 3: GPU Resources
jaws
  2 x NVIDIA Tesla V100 (32GB)
  5,120 CUDA + 640 Tensor cores each
twiki
  2 x NVIDIA Quadro RTX 8000 (48GB)
  4,608 CUDA + 576 Tensor + 72 RT cores each
9 x 2023 nodes
  4 x NVIDIA A100 (80GB)
  6,912 CUDA + 432 Tensor cores each
6 x 2024 nodes
  2 x NVIDIA L40S (48GB)
  18,176 CUDA + 568 Tensor + 142 RT cores each
> 500,000 GPU cores alone!

## Slide 4: GPU Resources
Type | Architecture | Memory | #cards | Nodes | CUDA Cores | RT Cores | Tensor Cores | 
Tesla V100 | Volta | 16GB | 1 | jaws | 5,120 | - | 640 | 
 |  | 32GB | 2 | thanos |  |  |  | 
Quadro RTX 8000 | Turing | 48GB | 2 | twiki | 4,608 | 72 | 576 | 
NVIDIA A100 | Ampere | 80GB | 36 | 9 x 2023 | 6,912 | - | 432 | 
NVIDIA L40S | Lovelace | 48GB | 12 | 6 x 2024 | 18,176 | 142 | 568 | 
 |  |  |  |  | 491,520 | 1,848 | 25,440 | 518,808

## Slide 5: Why do we use GPUs?
Both CPUs and GPUs work in fundamentally different ways:
A CPU handles the majority of the processing tasks for a computer.
  fast and versatile
  built to handle any number of required tasks
    accessing hard drive storage
    logging inputs
    moving data from cache to memory
  That means that CPUs can bounce between multiple tasks
A GPU is designed from the ground up to render high-resolution images and graphics almost exclusively
  This doesn’t require a lot of context switching
  GPUs focus on concurrency, or breaking down complex tasks.
Notes: This parallelisation is different to SLURM parallelisation from yesterday
  How many operations we can get through a specific set of resources at any one time

## Slide 6: Why do we use GPUs?
Advantages
  Incredible potential to speed up jobs
    Independent operations i.e., adding two matrices, applying image filters, processing sequence data
Disadvantages
  Limited resource (for now)
  Power requirements
    High power consumption compared to CPU
    Greater operations/Watt when used “properly”

## Slide 7: GPUs vs CPUs
CPU – 16C (32T) |  |  |  |  |  |  | 
GPU – >1000C

## Slide 8: GPUs vs CPUs
CPUs have to allocate more physical space on a chip to memory caches and controllers
  This is what allows for such low latency
  But limits the ability to do lots of simultaneous tasks
CPU
Control
Cache
Memory (DRAM)
ALU
ALU
ALU
ALU
GPU
Memory (VRAM)

## Slide 9: Speed Increases from Parallelisation
GPU
(High Throughput)
T1
T2
T3
T4
Processing
Idle
Ready
CPU
(Low Latency)
T1
T2
T3
T4
Notes: 10,000 images
12s/image CPU - >33hrs 8.3 kWh
0.5s/image GPU – 1hr 20 mins 1.33 kWh

## Slide 10: Allocating GPUs
If you need to use a GPU, you must specify the queue and ask for it:
Or define the relevant parameters in an sbatch file:
$ srsh --partition=gpu --gpus=1 …
srun: job <jobID> queued and waiting for resources
srun: job <jobID> has been allocated resources
#!/bin/bash
#SBATCH --partition=gpu
#SBATCH --gpus=1
…

## Slide 11: Allocating GPUs
Alternatively specific card types can be requested:
  --gpus=a100, rtx8000, v100, l40s
The number of cards requested can also be specified:
  --gpus= a100:[1-4], rtx8000:[1-2], v100:[1-2], l40s:[1-2]
$ sinfo -o "%50N %10c %20m %30G "
NODELIST CPUS MEMORY GRES
NODELIST CPUS MEMORY GRES
jennerator,n19-32-192-abomination,n19-32-192-antma 4+ 7000+ (null)
n19-24-192-jaws 48 180000 gpu:v100:2(S:0)
n21-16-256-twiki 32 250000 gpu:rtx8000:2
n23-64-512-aragog,n23-64-512-buckbeak,n23-64-512-c 128 495000+ gpu:a100:4
n24-64-384-angel,n24-64-384-anya,n24-64-384-darla, 128 386000 gpu:l40s:2

## Slide 12: Allocating GPUs
Simply requesting a GPU is often not enough so ensure that the job/tool is also appropriate for hardware acceleration
  GPU enabled versions of tools/pipelines
  Ensure any CLI options for hardware acceleration are used
Additionally, with the installation of the new nodes select resources that make sense for your application
  A100s – multi-GPU training, large models, and datasets
  L40S – single card training, inference
Select a GPU based on the utilisation of the GPU’s memory
  A100s – 80GB
  RTX 8000s – 48GB
  L40S – 48GB

## Slide 13: Monitoring GPU usage
Running nvitop –m from an active terminal on the will produce a top-like interface
  Driver and CUDA versions
  GPUs allocated to a particular job or located in a particular node
  Current GPU utilisation, VRAM usage, and Memory Bus utilisation and ticker of historic utilisation
  CPU and Memory usage
  Currently running processes
Very useful for setting up and monitoring a GPU job
  Maximising the size of a model/dataset
  View behaviour over time to spot any issues
Notes: Really useful for setting GPU parameters relating to dataset/model size

## Slide 14: Monitoring GPU usage
Driver and CUDA versions
Individual GPUs in the node
GPU Memory Usage in MB and %age total
Processes currently running
Graphical output of current memory usage and utilisation
Ticker showing utilisations over the last few minutes
Similar outputs for CPU and RAM usages
[fmacfarl@twiki ~]$ nvitop –m

## Slide 15: Examples
MQGLLILSVLLGAALGKEDFVGHQVLRITAADEAEVQTVKELEDLEHLQLDFWRGPGQPGSPIDVRVPFPSLQAVKVFLEAHGIRYRIMIEDVQSLLDEEQEQMFASQSRARSTNTFNYATYHTLDEIYDFMDLLVAEHPQLVSKLQIGRSYEGRPIYVLKFSTGGSNRPAIWIDLGIHSREWITQATGVWFAKKFTEDYGQDPSFTAILDSMDIFLEIVTNPDGFAFTHSQNRLWRKTRSVTSSSLCVGVDANRNWDAGFGKAGASSSPCSETYHGKYANSEVEVKSIVDFVKDHGNFKAFLSIHSYSQLLLYPYGYTTQSIPDKTELNQVAKSAVAALKSLYGTSYKYGSIITTIYQASGGSIDWSYNQGIKYSFTFELRDTGRYGFLLPASQIIPTAQETWLGVLTIMEHTVNNLY